## E50 C

PRODUCT DESCRIPTION

The model E50 C is a professional walk-behind scrubber-dryers, ideals for the cleaning of surfaces between 250 m² and 1.750 m².

With a cleaning width of 500mm and a speed of 3,5 km/h, this model boasts an area coverage of 1.750 m²/h.

Here after, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed several years;

- ESCS (Eureka Solution Control Stop-Valve) cuts off or activates the flow of solution upon brush command (standard on Trac version);

- Adjustable brushing head for an optimal traction stability on all type of floors;

- Adjustable solution flow;

- Parabolic squeegee with a double adjustment, equipped with LINATEX blades to grant a perfect drying;

- EDS (Eureka Dosing System) on board detergent dosing system (optional);

- Anti foam device;

- Adjustable pressure.

BRUSHES AND SQUEEGEE

- The E50 C has a cleaning width of 500mm, a squeegee width of 830 mm and boast an area coverage of 1.750 – 2.000 m²\h.

- The brush pressure can be adjusted from 0 to 37 kg.

- An electromagnetic valve (optional) starts the water flow slightly before the rotation of the brush or pad.

- Brush connection: the brush can be quickly connected/ disconnected without need for tools.

- Brush engine: direct drive to the brush (no belt).

- Brushing die cast aluminium  head equipped with protection wheels.

- The parabolic squeegee with double adjustment is equipped with LINATEX blades in order to grant an excellent drying.

Applications

It is suitable to clean all paved floors, internal and external like: ceramic tiles, marble, cement, linoleum, porcelain tiles and with any kind of dirt.

- Factories

- Communities

- Schools

- Churches

- Hospitals

- Swimming pools

- Airports

- Locker rooms

- Commercial centres

- Logistic centres

- Cleaning companies

- Restaurants

Standard ACCESSORIES

- NO TOOLS, easy BRUSH COUPLING SYSTEM

- ADJUSTABLE PRESSURE AND INCLINATION SQUEEGEE

- SELF-LEVELING BRUSH DECK SEALING RUBBER

- SUPERELASTIC, NON-MARKING FRONT TYRES

- WATER FLOW DOSING

- Adjustable brush pressure

OPTIONAL ACCESSORIES

- BRUSH IN PPL 0,9 – 0,6

- PAD HOLDER

- ABRASIVE BRUSH 1,2

- INOX SQUEEGEE (without blades)

- HOURMETER

- DETERGENT DOSING SYSTEM

- ESCS (Eureka Solution Control Stop Valve)

TRACTION

The E50C uses the following type of traction:

- Mechanical traction (operated by the rotation of the brush)

POWER SUPPLY

The E50 C is available in cable version only.

VACUUM ENGINE

The 2 stages vacuum engine, 230V - 400W – 1,8 AH creates a depression of 1183 mm/ H20.

TANKS

The tanks are 2 : the solution tank (40L) and the recovery tank (50L).The special design of the recovery tank and the big diameter draining pipe allow to empty completely the dirty water, IN A VERY SHORT TIME, without leaving any type of rest and without manual interventions.

COMPARISON SHEET – E50 C vs FIMAP MY 50 E and NILFISK CA531

| MAIN FEATURES | E50 C | FIMAP MY 50 E | NILFISK CA531 |
| --- | --- | --- | --- |
| Cleaning width | 500mm | 510mm | 530mm |
| Squeegee width | 830mm | 800mm | 760mm |
| Brush pressure | 0 - 37kgs | 25kgs | 30kgs |
| Naked machine weight | 76,5kgs | 62kgs | 135kgs |
| Productivity | 1.750 m²/h | 1.600 m²/h | 2.120 m²/h |
| Climbing rate | 3% | 2% | 2% |
| Brushes n° | 1 | 1 | 1 |
| Tanks capacity | 40 l – 50 l | 40 l – 40 l | 40 l – 40 l |
| Noise level | 73dB | - | 68dB |
| Water flow (l/m) | 0-2,5 | - | 0-1,8 |
| Rated power | 800W | 1.010W | 1.650W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 165 | 165 | 150 |
| Speed (km/h) | 3,5 | 3 | 3 |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 400 W | 560 W | - |
| Vacuum engine rated power | 400 W | 450 W | - |

COMPARISON SHEET – E50 base vs RCM GO 511 C and ADIATEK RUBY 50E

| MAIN FEATURES | E50 C | RCM GO 511C | ADIATEK RUBY 50E |
| --- | --- | --- | --- |
| Cleaning width | 500mm | 500mm | 485mm |
| Squeegee width | 830mm | 745mm | 740mm |
| Brush pressure | 0 - 37kgs | - | 35kgs |
| Naked machine weight | 76,5kgs | 68kgs | 70kgs |
| Productivity | 1.750 m²/h | 1.500 m²/h | 1.700 m²/h |
| Climbing rate | 3% | 3% | 2% |
| Brushes n° | 1 | 1 | 1 |
| Tanks capacity | 40 l – 50 l | 45 l – 48 l | 45 l – 48 l |
| Noise level | 73dB | - | - |
| Water flow (l/m) | 0-2,5 | - | - |
| Rated power | 800W | 1.300W | 1.200W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 165 | - | 180 |
| Speed (km/h) | 3,5 | 3 | 3,5 |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 400 W | - | 750 W |
| Vacuum engine rated power | 400 W | - | 450 W |