## TIGRA

PRODUCT DESCRIPTION

The TIGRA is a new ride-on vacuum sweeper designed and manufactured by Eureka to sweep small, medium and large areas.

Our major aim was to design a compact machine, fast and productive, that could be sold at a very competitive price.

The TIGRA is a modern alternative to bulky walk-behind or outdated/out-sized ride-on sweepers.

In fact, the TIGRA combines the maneuverability and user-friendliness of a walk-behind machine with the efficiency of a ride-on sweeper.

Thanks to its size, it fits very well through doorways and other narrow areas, and is particularly suitable for the cleaning of indoor hard surfaces as well as large carpeted areas.

It may also be suitable for a number of outdoor applications.

Its powerful and quiet electric drive enable the TIGRA to work at a very low level of noise.

Particular attention has been given to the external finish to give it a modern aesthetic appearance.

SWEEPING/VACUUMING SYSTEM

- Tigra has a main brush width of 650 mm, a total sweeping path of 1055 mm and a cleaning capacity, at full speed, of 5.486 sq\mt\hr.

- The unit operates on the overthrow principle, i.e. debris are thrown over the cylindrical brush into the waste container situated behind it.

- The brush is suspended in floating mounts, so that it adjusts automatically in order to compensate for wear and uneven surfaces.

- An innovative locking system enables the main brush to be replaced without tools.

- A bulk waste flap is installed in front of the brush and easily opened from the driver's seat. It allows the broom to pick up even bulkier debris.

- Like the main brush, the standard right side brush is activated from the control panel. A second (left) side brush is available as an option. Both brushes are mounted on side shock-absorbers to prevent damage.

- Fine dust is filtered through a polyester bag filter ( class USG ), which allows an excellent filtering rate ( 99,9% ) and has a much longer lasting life than traditional filters. The filter can be cleaned thanks to an efficient mechanical shaker.

- The container has a real capacity of 63 Lt. (or 83 Kg). It is equipped with wheels and it also has a convenient transport handle that allows the entire hopper to be rolled to the dump site.

- Visibility is excellent from the operator’s position, and all controls are simple and ergonomically located for easy operation.

- Maintenance access is convenient as well. The top lifts up to expose the battery compartment as well as motors and other service areas.

MAJOR APPLICATIONS AND TARGET GROUPS

Thanks to its size, the Tigra is particularly suitable for the cleaning of indoor hard surfaces as well as large carpeted areas. It may also be suitable for a number of outdoor applications.

- Food industry

- Trucking and warehousing

- Paper and allied products

- Chemical industry

- Cleaning contractors

- Shopping malls

- Car parks

- Large hotel areas

- Lumber and wood products

- Service stations

- Airports ( indoor areas )

- Breweries

- Standard solid rubber tyres ( non-marking type ) allow unlimited operations in areas with glass or metal splinters.

- The floating main broom enables the Tigra to work efficiently also on uneven floors.

- Working time on one battery charge is approx. 3 hours. This enables the Tigra to sweep between 10.140 and 16.458 sq.mt (based on theoretical cleaning capacity).

STANDARD ACCESSORIES

* Infinitely variable forward/reverse speed drive, electronically controlled

* SYSTEM MOTOR 24V - 600 W

* DRIVE MOTOR 24V - 400 W

* POLYESTER BAG FILTER

* CHEVRON TPYE MAIN BRUSH, FLOATING, RAPID REPLACEMENT WITHOUT TOOLS,

*  IN PPL, MIXED BRISTLES,  mm 650 x Ø 265 mm

* RETRACTABLE RH SIDE BRUSH , DIAMETER mm 450

* CONTROL PANEL INCLUSIVE OF :

* SYSTEM MOTOR KEY SWITCH - VACUUM CUT-OFF CONTROL

* FULL RUBBER,  NON-MARKING TIRES

* BRAKES : ELECTRIC SERVICE BRAKES , MECHANICAL PARKING BRAKES

*FLAP RAISING CONTROL FROM OPERATOR'S POSITION

*ADJUSTABLE SEAT, WITH SAFETY MICRO SWITCH

*PVC BUMPER

*DIRT CONTAINER MOUNTED ON WHEELS

*BATTERY CHARGE INDICATOR – HORN

*ACOUSTIC SIGNAL KIT FOR REVERSE SPEED

*FLASHING LIGHT (compulsory in EC countries)

OPTIONAL ACCESSORIES

*LEFT SIDE BRUSH

*HOURMETER

*REDUCTION REFUSE BOXES

*CARPET CLEANING KIT

*BATTERIES 6V – 240 Ah

*BATTERY CHARGER 24V-25A

*BATTERY TRAY (4 X 6V-240A)

*POLYESTER BAG FILTER “C” CLASS WITH POLIURETHAN

FEATURES AND BENEFITS

POWER EFFICIENCY:

- FRONT ELECTRIC WHEEL UNIT: The Tigra is equipped with a front electric wheel unit, hence we have considerably reduced the power consumption. We are therefore able to offer a lower purchase price, lower operational costs and lower cost of components. In addition, this system enables the machine to work at a very low noise level.

MANEUVERABILITY EFFICIENCY:

- VERY COMPACT SIZE FOR MAXIMUM MANEUVERABILITY IN NARROW SPACES

- VERY LOW TURNING RADIUS: 95 cm

- SIMPLE CONTROLS: One button controls both forward and reverse speed, while the drive is engaged by mean of a motorcycle type handle. Service and parking brakes are conveniently located on the steering handle.

- EXCELLENT VISIBILITY: The operator sits in front.

- Side brush(es) mounted on shock-absorbers: Additional protection against bumps or collisions.

- FULL RUBBER TIRES: You will not have to worry about checking air pressure or repair flats. Furthermore, wheels are of “non-marking” type as standard.

- PVC BUMPER: It offers additional protection against bumps or collisions.

FILTERING EFFICIENCY:

- POLYESTER BAG FILTER, CLASS G: Most competitor machines offer a single panel filter system which has disadvantages such as rapid clogging, dust coming out from the filter seals and a small filtering area. Tigra is equipped with a polyester bag filter which is particularly efficient for the retaining of fine dust and has a much longer lasting life than other traditional filters.

WASTE COLLECTION EFFICIENCY:

- BACK LOADING SYSTEM: Thanks to the position of the hopper, the Tigra offers better visibility and filling capacity.

- HOPPER MOUNTED ON WHEELS: It allows the hopper to be rolled to dump site without fatigue.

- MULTI-BRISTLES MAIN BRUSH: In order to enable the main brush ( 65 cm width ) to work on most floor types, we have designed a 2 sections bristle brush.  Integrated in the same brush are: a fine bristle section for fine dust and a thicker bristle section for heavier dust.

- FLOATING, SELF-ADJUSTING MAIN BRUSH: The main brush floats for better performances on uneven floors and automatically adjusts itself to compensate for wear and uneven surfaces.

USER FRIENDLY:

- ALL CONTROLS LOCATED AT DRIVER’S REACH: The main brush/side brush(es) can be lowered or raised from the floor thanks to a lever positioned on the dashboard , and can be activated or deactivated thanks to a control button.

- ADJUSTABLE SEAT: For extra operator’s comfort.

- The main brush can be quickly replaced without tools

- VACUUM-FAN CUT-OFF: It allows the machine to work efficiently also on wet areas.

- STRONG METAL STRUCTURE, COATED WITH EPOXY POWDER: Additional protection against bumps, collisions, and better protection against scratches or rust.

- EASY ACCESS FOR SERVICING: The top lifts up to expose the battery compartment as well as motors and other service areas.

- VERY COMPETITIVE PRICE!!

COMPARISON NOTES - TIGRA VS. KAERCHER KM 90/60 R \ NILFISK SR 1101

| 1. MAJOR CHARACTERISTICS | TIGRA | KM 90/60 R | NILFISK SR 1101 | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning path only main broom | mm 650 | mm 615 | mm 700 | 1 |
| Cleaning path main broom + 1 side broom | mm 850 | mm 900 | mm 980 | 2 |
| Cleaning path main broom + 2 side brooms | mm 1055 | mm 1150 | mm 1260 | 3 |
| Max. speed | 5,2 Km/h | 6,0 Km/h | 6 Km/h | 4 |
| Max. cleaning capacity | 5.486 m²/h at 5,2 Km/h | 6.900 m²/h | 5.900 m²/h | 5 |
| Capacity of dirt container ( volume ) | 63 Lt. | 60 Lt. | 70 Lt. | 6 |
| Loading system | Rear | Rear | Rear |  |
| 2. BRUSHES |  |  |  |  |
| Floating \ Self-leveling | YES | NO | - | 7 |
| Self-adjusting | YES | NO | - | 8 |
| Rapid replacement | YES | YES | NO | 9 |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 10 |
| Retractable side brushes | YES | YES | - | 11 |
| 3. FILTERING SYSTEM |  |  |  |  |
| Type of filter | Polyester bag | Polyester panel | Panel | 12 |
| Filter shaking system | Mechanical | Mechanical | Electric | 13 |
| 4. DRIVE SYSTEM |  |  |  |  |
| Type of drive | Battery operated ( 24 V ) | Battery operated ( 24 V ) | Battery operated ( 24 V ) |  |
| Type of drive | Electric wheel unit ( front ) | Electric wheel unit ( front ) | Electric wheel unit ( front ) |  |
| Speed control | Hand-grip + speed selector | 1 pedal fwd\rev | 1 pedal fwd\rev | 14 |
| Type of wheels | Full rubber - non marking | Pneumatic tires | Full rubber | 15 |
| Number of wheels | 3 ( 1 front \ 2 back ) | 3 ( 1 front \ 2 back ) | 3 ( 1 front \ 2 back ) |  |
| Turning radius | 950 mm | ? | 1000 mm | 16 |

COMPARISON NOTES - TIGRA VS. KARCHER KM 90/60 R / NILFISK SR 1101

| NOTE NUMBER | FEATURE\BENEFIT |
| --- | --- |
| 1\2\3\4\5 | The larger main brush combined to a larger overall sweeping path and a faster operational speed, allows for an overall larger working capacity and productivity. |
| 6 | The TIGRA’s hopper has a real capacity of 63 liters, larger than Karcher’s and Nilfisk-Advance’s. |
| 7\8 | The TIGRA’s brush is suspended in floating mounts so that it adjusts automatically to compensate for wear and uneven surfaces |
| 9 | An innovative locking system enables the main brush to be replaced without tools. |
| 10 | Integrated in the same brush are: a fine bristle section for fine dust and a thicker bristle section for heavier dust. TIGRA’s unique system allows for efficient performances on most floor\dirt types. |
| 11 | TIGRA’s side brush(es) offer additional protection against bumps or collisions. |
| 12 | TIGRA is equipped with a polyester bag filter which is particularly efficient for the retaining of fine dust, and has a much longer lasting life than other traditional filters. Our competitor machines offer a single panel filter system which has disadvantages such as rapid clogging and dust coming out from the filter seals. |
| 13 | TIGRA’s filter-shaker allows for an extremely efficient cleaning of the filter. |
| 14 | This system is much more user friendly and ergonomic than the “pedal” system. |
| 15 | Non-marking tires allow working on white floors without marking the area all over. |
| 16 | A smaller turning radius increases TIGRA’s maneuverability and allows for efficient work in narrow areas. |